## Slide 1: The 5G responses for the IoT challenges
Presenter: Bendek Kovács, PhD
(Senior Specialist, Network Performance, Ericsson)
5G
Notes: 11/28/20172012-02-03
1
2012-02-03
1

## Slide 2: Circuit switched fallback: LTE Data, CS voice
3G
LTE
HSPA
GSM
GSM
Packet Core
LTE
WCDMA
Circuit switched CORE
INTERNET, VPN, ETC.
Wi-Fi
No CS Support!
Authentication, Security, Connectivity, Mobility
Authentication, Security, Connectivity, Mobility
Telephony services
Data Services

## Slide 3: VoICE OVER LTE and Ims Centralized services
3G
LTE
HSPA
GSM
GSM
Packet Core
LTE
WCDMA
Circuit switched CORE
IMS Telephony
INTERNET or VIRTUAL PRIVATE NETWORK
Wi-Fi
CS Voice
Data
PS Voice
Data, Internet APN
Data
Data, Enterprise APN
Authentication, Security, Connectivity, Mobility
Data Services
Centralized telephony services

## Slide 4: Ericsson Paving the way to 5G
150 Mbps
300 Mbps
600 Mbps
Cat-1
Power Saving Mode
Extended Coverage
Narrowband-IoT
Ericsson Lean Carrier
1 Gbps

## Slide 5: 3GPP access technologies for massive ioT communications
Coverage
Battery life
Throughput (peak)
Security
Deployment
Mobility
EC-GSM-IoT
164dB (+20dB)
10+ Year
473/473kbps
SW
Cat-M1
160dB (+15dB)
10+ Year
0.8/1 Mbps full duplex
SW
Connected & idle mode mobility
NB-IoT
164dB (+20dB)
10+ Year
227/250kbps multi-tone UL
SW
Idle mode mobility
Bandwidth
600kHz
1.4MHz
200kHz
Idle mode mobility

## Slide 6: 5G networks…
LTE
Packet Core
LTE
IMS Telephony
INTERNET or PRIVATE NETWORK
Wi-Fi
Wi-Fi calling
PS Voice
Data
Data
Data
NB-IoT
5G NR
IoT Services
Application service
Media APP,
Netflix IPTV

## Slide 7: Ecosystem around the Massive IoT Infrastructure

## Slide 8: The massive iot challenge…

## Slide 9: connected park
Requirements: - Totally different traffic model (low and high bw, massive number of devices, rare communication) - Cheap device is required, low Operator ARPU - Low power devices are required - Heavily customized application - Security?, Positioning?, Zero touch management?, etc.
Connected park services: - From guessing to knowing, measure the health of the park - An intelligent maintenance system, an AR enabled worker - Vibration reports on tools - Remote operation - Customer services developed on popular common Platforms
Notes: Supporting a sustainable future for people, nature and businesses Create value for people, the city, and businesses Leveraging on the global and/or local eco systems of possible partners and data flows
https://www.youtube.com/watch?v=RZiyWAV4MW4

## Slide 10: IoT: Wide Range of Requirements
Massive Machine Type Communication
CAPILLARY NETWORKS
LOW COST, LOW ENERGY SMALL DATA VOLUMES MASSIVE NUMBERS
ULTRA RELIABLE VERY LOW LATENCY VERY HIGH AVAILABILITY
LOGISTICS, TRACKING AND FLEET MANAGEMENT
SMART AGRICULTURE
SMART BUILDING
REMOTE HEALTH CARE
Critical Machine Type Communication
SMART METER
TRAFFIC SAFETY & CONTROL
INDUSTRIAL APPLICATION & CONTROL
REMOTE MANUFACTURING, TRAINING, SURGERY
Notes: So when we think about the Internet of Things it’s easy to think of it as a single entity – but of course it’s not. It’s an enabler for a very wide variety of use cases and not unsurprisingly those use cases have differing requirements that need to be met to make them viable.
Two main classes of cases we talk about are these – massive machine type communication and critical machine type communication. In the first it’s all about cases that will roll out in high volume – quite possibly embedded with no access to on-grid power. In the second there’s more focus on safety, security and integrity. These are applications where trust in the system is essential – remote surgery could be an example– or automated braking in your car for instance. Many different MTC use cases with varying requirements for connectivity exist in between the two ends of the MTC scale.
We can see that there is a range of requirements that underpin these use cases – that are more or less relevant in each case. For the IoT to reach it’s potential we need to be able to deliver connectivity that meets these needs for reliability, for scale, for low energy use and low cost.
Cellular is the technology that can address maybe not all, but most of these needs and it has some specific properties that makes it attractive for a wide range of opportunities.
235 words - 2:10
Notes:
The requirements of machine-type communication (MTC) vary considerably. At one end of the scale lies massive MTC, with critical MTC services at the other end.
Examples that fall into this Massive MTC use-case category include the monitoring and automation of buildings and infrastructure, smart agriculture, logistics, tracking and fleet management. The requirements for massive MTC include: > architecturally simple devices that use a low-complexity transmission mode > devices that can run on battery power for many years > long transmission ranges for devices in remote locations > scalable networks that can connect either a large or a small number of M2M devices
In the Critical MTC type of communication, monitoring and control occur in real-time, E2E latency requirements are very low – at millisecond levels – and the need for reliability is high.
---------------------------------------------
Prepared for : IoT Launch 2015
Best Before: Jan 2016
Author : Shanqing Ullerstig & Paul Cowling – BURA Marketing & Communications
Source: Adjust slide from GF Research
-------------------------------------------------

## Slide 11: 5G networks…
LTE
Packet Core
LTE
IMS Telephony
INTERNET or PRIVATE NETWORK
Wi-Fi
Wi-Fi calling
PS Voice
Data
Data
Data
NB-IoT
5G NR
IoT Services
Application service
Media APP,
Netflix IPTV

## Slide 12: 5G networks…
LTE
Packet Core
LTE
IMS Telephony
INTERNET or PRIVATE NETWORK
Wi-Fi
Wi-Fi calling
PS Voice
Data
Data
Data
NB-IoT
5G NR
M-IoT Services
Application service
Media APP,
Netflix IPTV
C-IoT Services

## Slide 13: Network slicing
Ability to distinguish between fundamentally different services

## Slide 14: Example of Network slice types
Enterprise and Industry
Massive MTC
Massive MTC
Enhanced MBB
Enterprise and Industry
Critical Communication and MTC
Low cost
Low energy
Massive numbers
Wide area coverage
Internet access
Operator services
High availability
High reliability
Low latency
Very high availability
Very high reliability
Very low latency

## Slide 15: 5G networks…
LTE
Packet Core
LTE
IMS Telephony
INTERNET or PRIVATE NETWORK
Wi-Fi
Wi-Fi calling
PS Voice
Data
Data
Data
NB-IoT
5G NR
M-IoT Services
Application service
Media APP,
Netflix IPTV
C-IoT Services

## Slide 16: 5G network SLICING
LTE
TELECOM Packet Core
LTE
IMS Telephony
INTERNET or PRIVATE NETWORK
Wi-Fi
Wi-Fi calling
PS Voice
Data
Data
Data
NB-IoT
5G NR
IoT Services
Sensor
Media APP,
Netflix IPTV
IOT Packet Core
INDUSTRY Packet Core
ROBOT COntrol

## Slide 17: Cor network selection and deployment options
Network slices are network sharing common functions and / or infrastructure but built for a specific service or purpose
Core Network Selection
  PLMN ID based
  APN based
  Dedicated Core Network Selection
  enhanced Décor (eDecor)
  5G Core network selection

## Slide 18: Communication in the M-MTC Slice

## Slide 19: Short Message System (SMS)
Due to the available alternatives for cost efficient transport of data over the control plane (DoNAS), the main intention for using SMS in Massive IoT Infrastructure solution is to configure eUICC devices
SMS is a well-established method for simple device configuration and communication with simpler devices. SMS support is mandatory functionality for all IoT access types (EC-GSM, NB-IoT, Cat-M1)
SMS over SGs

## Slide 20: IP based communication over NAS (DoNAS)
Control plane vs Data plane
Data plane is originally designed for voice, media, high bw, etc. while control plane is designed for short messages.
DoNAS enables transport of non-time critical, small volumes of data between the UE and the application server, resulting in reduced signaling.
Encapsulating the data in NAS PDUs avoiding full cycle of connection procedures
Traffic model “infrequent small data”
Mandatory feature for NB-IoT devices

## Slide 21: Power saving

## Slide 22: Power Saving mode (PSM)
Low Complexity UE Support
  The MME stores the UE Radio Capability for Paging information and notifies the eNodeB of this information in the Paging message
Discontinuous reception (DRX) cycle
  UE specific time interval between monitoring downlink channels for paging messages like SMS, can be enlarged
Network Synchronized High Latency Communication
  SGW buffers the downlink data towards the device
Power Saving Mode (PSM)
  A UE in PSM is not immediately reachable for mobile terminating services
  similar to power-off, but the UE remains registered with the network and there is no need to re-attach or re-establish PDN connections
GOAL: to reduce the UE signaling both functionally and frequency

## Slide 23: Developer's view

## Slide 24: Application Lifecycle developer’s sketch…
Develop applications using OpenSource and existing IoT Platform developer ecosystems
Installation: installing 100 000+ sensors
  Plug and Produce (Industry 4.0)
Update/Upgrade and load application for the devices
Operate applications
The developer does not need to know 3GPP details

## Slide 25: 5G system architecture 3GPP TS 23.501 V1.0.0 (2017-06)
Reference point representation. shows the interaction that exist between the NF services in the network functions described by point-to-point reference point (e.g. N11) between any two network functions (e.g. AMF and SMF).
Service-based representation, where network functions (e.g. AMF) within the control plane enables other authorized network functions to access their services
Authentication Server Function (AUSF)
Core Access and Mobility Management Function (AMF)
Data network (DN), e.g. operator services, Internet access or 3rd party services
Network Exposure Function (NEF)
NF Repository Function (NRF)
Policy Control function (PCF)
Session Management Function (SMF)
Unified Data Management (UDM)
User plane Function (UPF)
Application Function (AF)
User Equipment (UE)
The 5G architecture is defined as service-based and the interaction between network functions is represented in two ways. Network functions within the 5GC Control Plane shall only use service-based interfaces for their interactions.
Notes: A split between Access and Mobility Management (AMF) and Session Management (SMF) has been introduced in the architecture.

## Slide 26: Service-based interface in 5GC Services and Operations
NF A
Request
Reply
NF B
NF Service A1 Consumer
NF Service B1 Consumer
NF Service A1 Producer
NF Service B1 Producer
Subscribe
Notify
Service Based Interface (SBI)
NF Service Operation
Common control protocol using e.g. HTTP based API, replacing protocols like e.g. Diameter
Enabling the integration with IoT Platforms (e.g. Azure, AWS, etc…)

## Slide 27
The evolution of networks is motivated by new services and cost reduction
Network slicing, parts of the network are purpose optimized
Data over signaling channels for power saving and efficient communication
Saving on signaling messages for IoT devices for power saving
Network exposure, programmability, simplification, “easy” user interface
Key Takeaways

## Slide 29: references
TR 23.799 Study on Architecture for Next Generation System
TR 28.801 Study on management and orchestration of network slicing for next generation network.
TS 23.501 System Architecture for the 5G System
TS 23.502 Procedures for the 5G System